## Slide 1: Algorithms for the leather nesting problem: application to a real automotive industry instance
Pedro Brás
Supervision:
Cláudio Alves and José Valério de Carvalho
Doctoral Program in
Industrial and Systems Engineering
Universidade do Minho
Escola de Engenharia
SEEUM 2011

## Slide 2: Presentation Structure
Introduction: Leather Nesting Problem
Case Study
Geometrical aspects
Constructive algorithm
VNS algorithm
GRASP algorithm
Computational results
Conclusions

## Slide 3: Introduction
Nesting Problem
Cutting and packing problem with strong geometrical component
Elements
  Small objects: car seat pieces
  Large objects: leather hides
Problem
  Find a configuration of a given set of pieces on leather hides
Objective
  Minimize waste / Maximize the space occupied by the pieces on the leather hide
Restrictions
  Non-overlapping
  Quality zones and defects in small and large objects
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 4: Case Study
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 5: Geometrical aspects Shapes representation
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction
Notes: Número médio de vértices por:
. Peça: 200 (antes) e 80 (depois)
. Pele: 800 (antes) e 300 (depois)

## Slide 6: Geometrical aspects No-Fit-Polygon
Polygon representing the region that divides a legal placement of an illegal one (overlapping).
Given two polygons A and B, the NFPAB (No-Fit-Polygon) is the polygon that results from the locus of a reference point of polygon A when this polygon travels around the polygon B.
B
A
Reference point
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 7: Geometrical aspects No-Fit-Polygon
B
C
D
W
A
C
D
W
B
D
W
C
W
D
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 8: Constructive algorithm
Strategies
  Grouping the pieces (GRP)
  Selecting the next piece to place (SEL)
  Selecting a feasible placement region inside the hide (PLAC)
  Evaluate a given placement position (EVAL)
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 9: Constructive algorithm Strategies for grouping the pieces (GRP)
Area
Irregularity
Concavity
Length/height ratio
Quality area value
Homogeneity between quality zones
Mix function
a
l
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 10: Constructive algorithm Strategies for selecting the next piece to place (SEL)
By decreasing weight value;
Smallest IFP;
Biggest IFP;
Value provided by the function used to evaluate the placement positions.
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 11: Constructive algorithm Strategies for selecting a feasible region where to place the next piece (PLAC)
All the empty spaces on the hide;
Vertical levels;
IFP features:
  Smallest piece IFP;
  Biggest piece IFP;
  Smallest or biggest IFP, depending on the group of the selected piece;
Hide empty spaces features:
  Smallest/biggest empty space;
  Worst/Better overall quality;
  More/Less irregularity.
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 12: Constructive algorithm Strategies to evaluate a given placement position (EVAL)
Area of intersection between piece offset and layout:
  Total or partial area;
  Quality zones matching;
  Absolute and relative values;
Number of empty spaces;
Created waste;
Piece distance to:
  Hide border/center;
  Best/worst quality zones.
Piece
Piece offset
Offset intersection 1
Q1
Q2
Offset intersection 2
Qx
Piece
Piece offset
Offset intersection
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction
Notes: (E1) ∑2_(𝑖=1)^|𝐼|▒〖𝑎𝑟𝑒𝑎(𝐼_𝑖)〗: área total da intersecção de 𝑂 com o plano de corte actual e com a região exterior da pele;
(E2) 〖∑2_(𝑖=1)^|𝐼|▒〖𝑎𝑟𝑒𝑎(𝐼_𝑖)〗〗∕〖(𝑎𝑟𝑒𝑎(𝑂)−𝑎𝑟𝑒𝑎(𝑃))〗: área relativa da intersecção de 𝑂 com o plano de corte actual e com a região exterior da pele;
(E3) 〖𝑚𝑎𝑥〗_(𝑖=1, …|𝐼| ) 𝑎𝑟𝑒𝑎(𝐼_𝑖): área do maior polígono resultante da intersecção de 𝑂 com o plano de corte actual e com a região exterior da pele;
(E4) 〖〖𝑚𝑎𝑥〗_(𝑖=1, …|𝐼| ) 𝑎𝑟𝑒𝑎(𝐼_𝑖)〗∕〖(𝑎𝑟𝑒𝑎(𝑂)−𝑎𝑟𝑒𝑎(𝑃))〗: área relativa do maior polígono resultante da intersecção de 𝑂 com o plano de corte actual e com a região exterior da pele;
(E5) área da intersecção de 𝑂 com o plano de corte actual e com a região exterior da pele a somar ao total da área das zonas de qualidade de 𝑃 que estão sobre zonas de qualidade equiparáveis da pele;
(E6) área relativa da intersecção de 𝑂 com o plano de corte actual e com a região exterior da pele a somar ao total da área das zonas de qualidade de 𝑃 que estão sobre zonas de qualidade equiparáveis da pele;
(E7) área da intersecção de 𝑂 com o plano de corte actual e com a região exterior da pele a somar ao total da área das zonas de qualidade de 𝑃 que estão sobre zonas de qualidade B, C ou D da pele;
(E8) área relativa da intersecção de 𝑂 com o plano de corte actual e com a região exterior da pele a somar ao total da área das zonas de qualidade de 𝑃 que estão sobre zonas de qualidade B, C ou D da pele;
(E9) número de espaços vazios gerados pelo posicionamento de 𝑃;
(E10) área total do desperdício gerado pelo posicionamento de 𝑃;
(E11) distância de 𝑃 ao bordo da pele;
(E12) distância de 𝑃 ao centro da pele;
(E13) distância de 𝑃 à região com menor nível de qualidade da pele;
(E14) distância de 𝑃 à região com maior nível de qualidade da pele.

## Slide 13: VNS algorithm
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 14: VNS algorithm
Initial solution given by constructive algorithm:
    (G1) Piece area;
    (S2.D.1.c) Selection of the piece with the largest or smallest IFP depending on the selected group of pieces;
    (P6) The largest or smallest IFP depending on the group of the selected piece;
    (E11) Distance to the border of the hide.
Neighborhood structures:
    4 types of distinct movements.
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 15: VNS algorithm Movement M1
1: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | s6 |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Placement sequence S
 | u1 |  | u2 |  | u3 |  | u4 |  | u5 |  | u6 |  | u7 |  | u8 |  | u9 |  | u10 |  | … |  | u¦S¦ | (Material usage)
2: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | s6 |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Material usage window
 | u1 |  | u2 |  | u3 |  | u4 |  | u5 |  | u6 |  | u7 |  | u8 |  | u9 |  | u10 |  | … |  | u¦S¦ | 
3: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | p |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Worst fitness value
4: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | p’ |  | Constructive heuristic |  |  | Replace piece p by piece p’
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 16: VNS algorithm Movement M2
1: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | s6 |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Placement sequence S
 | u1 |  | u2 |  | u3 |  | u4 |  | u5 |  | u6 |  | u7 |  | u8 |  | u9 |  | u10 |  | … |  | u¦S¦ | (Material usage)
2: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | s6 |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Material usage window
 | u1 |  | u2 |  | u3 |  | u4 |  | u5 |  | u6 |  | u7 |  | u8 |  | u9 |  | u10 |  | … |  | u¦S¦ | 
3: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | p |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Worst fitness value
4: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | p’ |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Replace piece p by piece p’
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 17: VNS algorithm Movement M3
1: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | s6 |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Placement sequence S
 | u1 |  | u2 |  | u3 |  | u4 |  | u5 |  | u6 |  | u7 |  | u8 |  | u9 |  | u10 |  | … |  | u¦S¦ | (Material usage)
2: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | s6 |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Material usage window
 | u1 |  | u2 |  | u3 |  | u4 |  | u5 |  | u6 |  | u7 |  | u8 |  | u9 |  | u10 |  | … |  | u¦S¦ | 
3: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | p |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Worst fitness value
4: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | p |  | s7 |  | s8 |  | s9 |  | p’ |  | … |  | s¦S¦ | Swap piece p with piece p’
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 18: VNS algorithm Movement M4
1: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | s6 |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Placement sequence S
 | u1 |  | u2 |  | u3 |  | u4 |  | u5 |  | u6 |  | u7 |  | u8 |  | u9 |  | u10 |  | … |  | u¦S¦ | (Material usage)
2: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | s6 |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Material usage window
 | u1 |  | u2 |  | u3 |  | u4 |  | u5 |  | u6 |  | u7 |  | u8 |  | u9 |  | u10 |  | … |  | u¦S¦ | 
3: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  | p |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Worst fitness value
4: | s1 |  | s2 |  | s3 |  | s4 |  | s5 |  |  |  | s7 |  | s8 |  | s9 |  | s10 |  | … |  | s¦S¦ | Remove piece p
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 19: GRASP algorithm
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 20: GRASP algorithm Constructive phase
Restricted candidate list (RCL): 10 pieces with the smallest IFP area;
Next piece to place: Random selection from RCL;
Feasible placement region: Selection of the smallest piece IFP;
Placement position evaluation: Distance between piece and the border of the hide.
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 21: GRASP algorithm Improvement phase
Local search procedure;
Neighborhood given by M1 movement
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 22: Computational results: Constructive algorithm
Strategies comparative analysis
    Grouping the pieces (GRP):
      Area;
      Quality zones;
    Selecting the next piece to place (SEL) and selecting a feasible region where to place the next piece (PLAC):
      IFP features;
    Placement evaluation (EVAL):
      Offset intersection between piece and layout.
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 23: Computational results: Constructive algorithm
Performance results
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction
Notes: 5:
  (G5) valor das peças baseado nas suas zonas de qualidade e respectivas áreas;
  (S2.D.1.c) selecção da peça com o maior ou o menor IFP de acordo com o grupo de peças seleccionado.
  (E1) ∑2_(𝑖=1)^|𝐼|▒〖𝑎𝑟𝑒𝑎(𝐼_𝑖)〗: área total da intersecção de 𝑂 com o plano de corte actual e com a região exterior da pele;
12:
  (G5) valor das peças baseado nas suas zonas de qualidade e respectivas áreas;
  (S1.D) selecção de uma peça a partir do conjunto completo de peças ordenadas por ordem crescente (S1.I) ou decrescente (S1.D) do valor de um determinado atributo;
  (P6) o maior ou menor IFP da peça, dependendo do grupo da peça seleccionada;
  (E1) ∑2_(𝑖=1)^|𝐼|▒〖𝑎𝑟𝑒𝑎(𝐼_𝑖)〗: área total da intersecção de 𝑂 com o plano de corte actual e com a região exterior da pele;
6, 7, 8, 9 e 10:
  (G5) valor das peças baseado nas suas zonas de qualidade e respectivas áreas;
  (S2.D.1.c) selecção da peça com o maior ou o menor IFP de acordo com o grupo de peças seleccionado.
  (E12.MAX), (E14.MIN), (E14.MAX), (E13.MIN) e (E13.MAX) distâncias a…

## Slide 24: Computational results: VNS algorithm
Tuning stage
    Neighborhood structures performances:
      Best performance for combination of all neighborhood;
    Size of material usage window:
      Best results for window [10%;50%] of hide yield;
    Size of candidate list for removal:
      Best results considering 3 candidates for removal
    Size of candidate list for insertion:
      Best results considering 3 candidates for insertion
    Neighborhood exploration sequence
      Best results for sequence N1, N2, N3 e N4.
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 25: Computational results: VNS algorithm
Performance results
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 26: Computational results: GRASP algorithm
Performance results
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 27: Conclusions
Algorithms development for leather nesting problems::
    Constructive heuristic;
    VNS meta-heuristic;
    GRASP meta-heuristic;
Accomplishment of extensive computational experiments:
    Quality of material usage efficiency;
    Clear improvements given by VNS and GRASP meta-heuristics;
Feasible algorithm integration into:
    Decision support tools;
    Automation of leather cutting process.
Case study
Geom. aspects
Construct. algorithm
VNS algorithm
GRASP algorithm
Results
Conclusions
Introduction

## Slide 28: Publications
Alves, C., Brás, P., Valério de Carvalho, J., and Pinto, T.
New constructive algorithms for leather nesting in the automotive industry.
Computers & Operations Research, (2011).
Alves, C., Brás, P., Valério de Carvalho, J., and Pinto, T.
A variable neighborhood search algorithm for the leather nesting problem.
(accepted) Mathematical Problems in Engineering, (2011).
Brás, P., Alves, C., Valério de Carvalho, J., and Pinto, T.
Exploring New Constructive Algorithms for the Leather Nesting Problem in the Automotive Industry. 5th International Conference on Management and Control of Production and Logistics, International Federation of Automatic Control (IFAC), Coimbra, Portugal, (2010).
Brás, P., Alves, C., Valério de Carvalho, J., and Pinto, T.
Irregular Shape Packing on Leather Hides using GRASP: a Real Case Study.
International Conference on Engineering UBI2011 – “Innovation and Development”, Covilhã, Portugal, (2011).
Brás, P., Alves, C. and Valério de Carvalho, J.
Algorithms for industrial process optimization: An application in the automotive industry.
Semana da Escola de Engenharia, (2011).

## Slide 29: Obrigado!
Thank you!