## Slide 1
University of Minho School of Engineering Centre of Biological Engineering | 
Uma Escola a Reinventar o Futuro – Semana da Escola de Engenharia - 24 a 27 de Outubro de 2011
JOANA I. ALVES*
Supervisors: Madalena Alves, Diana Z. Sousa
* joana.alves@deb.uminho.pt
microbial syngas conversion by MESOPHILIC AND thermophilic anaerobic mixed-cultures
Introduction
Methods
Synthesis gas (or syngas) can be produced from the gasification of a variety of recalcitrant or biodegradable waste materials. Syngas is a mixture composed of mainly H2, CO and CO2 that can be used in a biological process for the production of fuels or usable chemicals. The main goal of this work was to study the physiology and microbial composition of anaerobic cultures able to utilize syngas.
CO, H2 and CO2
Fuels
Usable chemicals
Total pressure = 1.75 bar
 | CO | H2 | CO2
Syngas from coal gasification | 60% | 30% | 10%
Syngas was diluted with H2/CO2 (80:20 v/v) to provide CO concentrations ranging from 5% to 50% CO to the cultures.
Thermophilic
suspended slugde from a reactor treating organic municipal solid wastes
Mesophilic suspended slugde from a labscale bioreactor
Substrate (series M1, T1 and T2)
Enrichment cultures
Substrate (series T2)
CO diluted with N2 to provide CO concentrations from 10% to 50% CO to the cultures.
Gas composition (gas chromatography), soluble fermentation products (liquid chromatography)
Microbial growth (spectrophotometry, abs 600 nm)
Microbial communities (16S rRNA based PCR-DGGE, cloning and sequencing)
Monitoring
37 °C
55 °C
Results
Mesophilic enrichment series
Substrate: CO concentration: | Syngas (3 transfers) 5% to 10%
M1
Thermophilic enrichment series
Substrate: CO concentration: | Syngas (4 transfers) Syngas (12 transfers) 5% to 50% | Syngas (4 transfers) CO (8 transfers) 5% to 50%
T1
T2
After 2 transfers the biomass also lost the ability to produce methane, that was being produced during 1st transfer.
After 2 transfers there were no growth, neither syngas or CO conversion.
T1
T2
(after 16 transfers)
(after 12 transfers)
Conclusions
Acknowledgements
The financial support from Fundação para a Ciência e Tecnologia (FCT) and European Social Fund (POPH-QREN) trough PhD grant SFRH/BD/48965/2008 given to Joana Alves is gratefully acknowledged.
References
Basu R et al. (1993) Report for U.S. Department of Energy, 1-32.
Henstra AM et al. (2007) Current Opinion in Biotechnology, 18(3) 200-206.
Hussain A et al. (2011) Appl Microbiol Biotechnol, 90:827-836.
Oelgeschlager E and Rother M (2008) Arch Microbiol, 190:257-269.
Sipma J et al. (2006) Critical Reviews in Biotechnology, 26:41–65.
Sokolova TG et al. (2009) FEMS MicrobiolEcol, 68:131-141.
Worden RM et al. (1997) American Chemical Society, 321-335.
Regarding CO consumption, the thermophilic suspended sludge offers potential advantages over the mesophilic suspended sludge.
T2
I
T1
I
>
>
>
>
1
>
>
>
>
2
>
>
>
>
1
2
>
>
>
>
>
>
Desulfotomaculum sp. Hbr7 (99% identity)
Desulfotomaculum australicum str. AB33 (98%)
Thermophilic anaerobic bacterium K1L1 (96%)
Thermoanaerobacterium aotearoense (86%)
CO degradation was faster on T1, probably because the substrate used during the initial 4 transfers was the same as during the entire experiment.
The diversity of the microbial community present, decreased drastically from the inoculum sample, suggesting a fast specialization of microbial community on this type of substrate.
This work gave insight into the microbiology and physiology of syngas and carbon monoxide conversion by anaerobic mixed culture.