## Slide 1
University of Minho School of Engineering Cnetr of Biological Engineering | 
Uma Escola a Reinventar o Futuro – Semana da Escola de Engenharia - 24 a 27 de Outubro de 2011
Why?
BRUNA FONSECA*
Supervisor: Maria Teresa de Jesus Simões Campos Tavares
* bfonseca@deb.uminho.pt
SOILS CONTAMINATED WITH HEXAVALENT CHROMIUM - SORPTION, MIGRATION AND REMEDIATION
How?
Results (Highlights)
CAUSES
Bioacumulation of Heavy Metals
What about Europe?
Target
Figure 1. Overview of contaminants affecting soil and groundwater and the status of identification and clean-up of contaminated sites in Europe, as reported to the European Environment Agency through the EIONET priority data flows on contaminated sites.
Hexavalent Chromium: Cr(VI)
Highly mobile
Exists mainly as oxyanions
Cr2O72-
CrO42-
HCrO42-
Toxic
Carcinogenic
Sampling
Sorption and Migration
Main characteristics
Loamy sand soil
Slightly acidic [pH=5.9]
Poor in organic matter [3.5%]
Sorption and Migration
Batch tests
Flow tests
The soil was collected near an automobile repair shop, in a zone of great agricultural activity.
Tested parameters
pH of the contaminant solution;
Concentration of the contaminant solution.
Competition with other heavy metals in solution;
Mathematical Modelling
First order rate equation
Power function
Freundlich equation
Langmuir equation
Sorption kinetics
Sorption equilibrium
Two-site non-equilibrium adsorption model
Electroremediation/Biobarriers
E = 10 V
Cr2O72-
Cr2O72-
Cr2O72-
Biobarrier
Bacteria:
Arthrobacter Viscosus
(Cr6+ → Cr3+)
Support:
Activated carbon or Zeolite
Kaolinite
[Cr(VI)] = 50 mg kg-1
Analysis
Total Chromium
USEPA 3051
Microwave acid digestion
Flame Atomic Absorption
Hexavalent Chromium
USEPA 3060A
Alkaline digestion
USEPA 7196A
Colorimetric method
The maximum sorption capacity decreases with pH and concentration increasing
Best fit
The rate constant increases with the solution concentration
Sorption kinetics: Single systems with Cr(VI)
pH2
pH5
Figure 2. Variation of mass o Cr(VI) adsorbed per mass of soil, for different initial solutions, at pH 2 and pH 5, respectively (C1=75 mg L-1;C2=92 mg L-1;C3= 128 mg L-1).
Acknowledgments
The author gratefully acknowledge the Fundação para a Ciência e Tecnologia, Ministério da Ciência e Tecnologia, Portugal by her PhD grant (SFRH/BD/27780/2006).
Rcarbon > Rzeolite
Electroremediation/Biobarriers
In general…
Conversion18d ≃ Conversion9d
Removal18d > Removal9d
For Activated Carbon…
Conversion18d >Conversion9d
Removal18d > Removal9d
Chart: C/%
| Zeolite | Activated Carbon | Blank
9 Days | 43.6911 | 17.2331
18 Days | 45.049 | 44.1979
Chart: R/%
| Zeolite | Activated Carbon | Blank
9 Days | 46.5959 | 21.5899
18 Days | 59.5461 | 79.1803
Figure 4. Fraction of Cr(VI) reduced to Cr(III) - C/% - and total removal of the Cr(VI) - R/%.
Biobarriers
Blank
Chart: (w//w0)/%
| Anode | 1 | 2 | 3 | 4 | 5 | Cathode
Cr(VI) | 76.9184 | 7.4772 | 3.7051 | 3.2115 | 4.1909 | 2.89 | 1.6069
Recovery = 100 %
Figure 3. Distribution of the Cr(VI) across the electrokinetic cell
Cr(VI) oxyanions migrated towards the anode chamber.
R = 77 %